## Slide 1: ENGI 301 Tap Test Device Proposal
2/19/24
Gloria Ni

## Slide 2: Diagnosing Severity of Hand Tremors
Current Solution: The “Tapping Test”
  Used to screen for tremors and ataxia (presence)
  Part of the Assessment and Rating of Ataxia (SARA)
  Procedure:
    Patient takes a pen and repeatedly taps it as fast as they can
    Doctor listens to the speed and degree of regularity of the rhythm
  Issue: very subjective – can be used to detect if there is a problem but not so much the severity of it
Device Goals
  Allow doctor to quantitatively assess severity of tremor
    Provide overall mean tapping frequency
    Provide standard deviation and range in tapping frequency
  Provide an intuitive user interface for both the patient and the doctor
    LCD screen to display results to the doctor
    LED to signal to the patient when to start or stop tapping
  Low cost → increased accessibility compared to motion sensors

## Slide 3: System Block Diagram
Pocket Beagle
TTP223B Capacitive Touch Sensor
I2C IIC 1602 LCD
GPIO
SPI0
Green LED
GPIO 59

## Slide 4: Power Block Diagram
Pocket Beagle
3.3 V
VOUT (5V)
Green LED (3.0-3.2V)
3.3 V
GND
GND
GND
TTP223B Capacitive Touch Sensor (2.2-5V)
I2C IIC 1602 LCD (5V)

## Slide 5: Components / Budget
Component | ENGI301 to Buy? | Cost
TTP223B Digital Capacitive Touch Sensor | Yes | 8.49
Green LED | No | 4.98
I2C IIC 1602 LCD Display Module | Yes | 10.99
Total |  | 24.46